## Slide 1: CS 456/656 Computer Networks
Mina Tahmasbi Arashloo and Bo Sun
Fall 2024
Lecture 5: Transport Layer – Part 1

## Slide 2: A note on the slides
Adapted from the slides that accompany this book.
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
All material copyright 1996-2023
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 3: Transport layer: roadmap
Transport-layer overview
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 4: Transport layer: roadmap
Transport-layer overview
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 5: Transport layer: overview
Provide service to the application layer
  Transport to Application: “If you give me some data and the ID of the other communication endpoint (e.g., the (IP, port) for the destination socket), I will get the data to that communication endpoint.”
Using the services of the network layer
  Network to transport: “If you give me some data and the ID of the computer (host) that is the destination (e.g., the IP address for the host), I will get the data to that destination host."
Notes: In each kind of network, the services of the network layer could be different, so let’s look at the Internet as an example.

## Slide 6: Transport layer: in the Internet
Application
Transport
Network (IP)
Link
Host ()
Physical
App 1
App N
…
Application
Transport
Network (IP)
Link
Host ()
Physical
App 1
App M
…
Notes: \

## Slide 7: Transport layer: in the Internet
Application
Transport
Network (IP)
Link
Physical
App 1
App N
…
Application
Transport
Network (IP)
Link
Physical
App 1
App M
…
I would like to send these 3000B to Socket on host
We can all collaborate to try to send packets of size 1500B from to , but they can get lost or reordered.
Host ()
Host ()
Notes: \

## Slide 8: Transport layer: in the Internet
Application
Transport
Network (IP)
Link
Physical
App 1
App N
…
Application
Transport
Network (IP)
Link
Physical
App 1
App M
…
I would like to send these 3000B to Socket on host
Transport-layer protocols bridge this gap
We can all collaborate to try to send packets of size 1500B from H1 to H2, but it can get lost or reordered.
Host ()
Host ()
Notes: \

## Slide 9: Transport layer: in the Internet
Application on host : send these 3000B through socket to socket on host
The network layer: I’ll do my best to get packets of size 1500B from to , but it may get lost or corrupted, or get to later than some earlier packets you send from .
Transport-layer protocol:
  How can I distinguish between traffic from different sockets?
  How do I break data into packets and put it back together?
  How do I make sure all bytes are delivered reliably?

## Slide 10: Transport layer: in the Internet
Application on host : send these 3000B through socket to socket on host
The network layer: I’ll do my best to get packets of size 1500B from to , but it may get lost or corrupted, or get to later than some earlier packets you send from .
Transport-layer protocol:
  How can I distinguish between traffic from different sockets?
  Port numbers, Multiplexing and Demultiplexing
  How do I break data into packets and put it back together?
  Segmentation and reassembly
  How do I make sure all bytes are delivered reliably?
  Reliable data transfer

## Slide 11: Transport Layer: in the Internet
physical
link
network
application
physical
link
network
application
transport
Sender:
app. msg
is passed an application-layer message
Attached its own metadata (header) to help with (de)mux, segmentation and reassembly, and reliable data delivery
creates segment (transport header + data)
passes segment to the network layer
transport
Th
Th
app. msg
Notes: May modify the segmentation and reassembly a bit

## Slide 12: Transport Layer: in the Internet
physical
link
network
application
physical
link
network
application
transport
transport
Receiver:
app. msg
extracts application-layer message
use header values to reassemble bytes if needed
receives segment (transport header + data) from network layer
Th
app. msg
use header values to demultiplex message up to application via socket.

## Slide 13: Two principal Internet transport protocols
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
TCP: Transmission Control Protocol
  segmentation and reassembly
  reliable, in-order delivery
UDP: User Datagram Protocol
  no segmentation and reassembly
  no reliability or ordering guarantees
  no-frills extension of “best-effort” IP protocol in the network layer
Both do mux and demux between sockets
services not available:
  delay guarantees
  bandwidth guarantees

## Slide 14: Transport layer: roadmap
Transport-layer overview
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 15: Multiplexing/demultiplexing
App
Transport
Network
Link
Transport
Network
Link
Network
Link
Host
Host
Router
End-to-end communication
Physical
Physical
Physical
App
App
App
App
App
handle data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing as sender:
multiplexing
?
de-multiplexing
use header info to deliver
received segments to correct
socket
demultiplexing as receiver:
Need an extra identifier!

## Slide 16
Multiplexing

## Slide 17: How demultiplexing works
host receives datagrams
  each datagram has source network address, destination network address (e.g., IP addresses)
  each datagram carries one transport-layer segment
  each segment has source, destination port number
host uses network addresses (e.g., IP addresses) & port numbers to direct segments to appropriate sockets
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format

## Slide 18: Connectionless demultiplexing
Recall:
when creating socket, must specify host-local port #:
serverSocket.bind((‘’, 12000))
when receiving host receives UDP segment:
  checks destination port # in segment
  directs UDP segment to socket with that port #
when sending data into UDP socket, must specify
  destination IP address
  destination port #
IP/UDP datagrams with same dest. port #, but different source IP addresses and/or source port numbers will be directed to same socket at receiving host
UDP sockets are identified with a pair of IP and port

## Slide 19: Connectionless demultiplexing: an example
serverSocket.bind((‘’, 6428))
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
mySocket1.bind((‘’, 5775))
mySocket2.bind((‘’, 9157))
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?

## Slide 20: Connection-oriented demultiplexing
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
server may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
  each socket associated with a different connecting client
demux: receiver uses all four values (4-tuple) to direct segment to appropriate socket

## Slide 21: Connection-oriented demultiplexing: example
transport
application
physical
link
network
P1
transport
application
physical
link
P4
transport
application
physical
link
network
P2
host: IP address A
host: IP address C
network
P6
P5
P3
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
server: IP address B
Three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets

## Slide 22: Summary of (de)multiplexing
Multiplexing, demultiplexing: based on transport segment and network datagram header field values
UDP: demultiplexing at the destination host using destination IP and port number (only)
TCP: demultiplexing at the destination host using 4-tuple: source and destination IP addresses, and port numbers
Notes: We don’t really talk about this?

## Slide 23: Transport layer: roadmap
Transport-layer overview
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 24: UDP – User Datagram Protocol
How does UDP distinguish between traffic from different sockets?
  Already covered in (de)multiplexing section
How does UDP break data into packets and put it back together ?
  It doesn’t! You can only put as much data into a UDP segment that will fit into a single packet. Otherwise, it will give the application an error.
How does UDP make sure all bytes are delivered reliably?
  It doesn’t!
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be lost or delivered out-of-order to app
Why do we have UDP again?

## Slide 25: UDP: User Datagram Protocol
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out-of-order to app
Connectionless?:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others

## Slide 26: UDP: User Datagram Protocol
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out-of-order to app
no connection establishment (which can add RTT delay)
simple: no connection state at sender, receiver
small header size
no congestion control
  UDP can blast away as fast as desired!
  can function in the face of congestion
Why is there a UDP?
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others

## Slide 27: UDP: User Datagram Protocol
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  HTTP/3
  Other network apps or protocols like DNS and SNMP (discussed later)
if reliable transfer needed over UDP:
  add needed reliability at application layer

## Slide 28: UDP: User Datagram Protocol [RFC 768]
Notes: read this RFC – it’s only 2.5 pages!

## Slide 29: UDP: Transport Layer Actions
transport
(UDP)
physical
link
network (IP)
application
transport
(UDP)
physical
link
network (IP)
application

## Slide 30: UDP: Transport Layer Actions
transport
(UDP)
physical
link
network (IP)
application
transport
(UDP)
physical
link
network (IP)
application
UDP sender actions:
app msg
is passed an application-layer message
determines UDP segment header fields values
creates UDP segment
passes segment to IP
UDPh
UDPh
app msg

## Slide 31: UDP: Transport Layer Actions
transport
(UDP)
physical
link
network (IP)
application
transport
(UDP)
physical
link
network (IP)
application
UDP receiver actions:
app msg
extracts application-layer message
checks UDP checksum header value
receives segment from IP
UDPh
app msg
demultiplexes message up to application via socket

## Slide 32: UDP segment header
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
length, in bytes of UDP segment, including header
data to/from application layer

## Slide 33: UDP checksum
Transmitted: 5 6 11
Goal: detect errors (i.e., flipped bits) in transmitted segment
Received: 4 6 11
1st number
2nd number
sum
receiver-computed
checksum
sender-computed
checksum (as received)
=

## Slide 34: Internet checksum
sender:
treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment content
checksum value put into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  not equal - error detected
  equal - no error detected.
  But maybe errors nonetheless?
  More later ….
Goal: detect errors (i.e., flipped bits) in transmitted segment
no error detected.

## Slide 35: Internet checksum: an example
example: add two 16-bit integers
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1

## Slide 36: Internet checksum: weak protection!
example: add two 16-bit integers
sum
checksum
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
0 1
1 0
Even though numbers have changed (bit flips), no change in checksum!

## Slide 37: Summary: UDP
“no frills” protocol:
  segments may be lost, delivered out of order
  best effort service: “send and hope for the best”
UDP has its benefits:
  no setup/handshaking needed (no RTT incurred)
  helps with reliability (checksum)
  …
build additional functionality on top of UDP in application layer