## Slide 1: CS 456/656 Computer Networks
Mina Tahmasbi Arashloo and Bo Sun
Fall 2024
Lecture 15: Link Layer – Part 2

## Slide 2: A note on the slides
Adapted from the slides that accompany this book.
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
All material copyright 1996-2023
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 3: Link layer: roadmap
Link layer overview
  Local Area Networks (LANs)
Switched LANs
  Ethernet and Addressing
  Address Resolution Protocol (ARP)
  Switches
Virtual LANs (VLANs)
Shared LANs and multiple access protocols

## Slide 4: Virtual LANs (VLANs): motivation
Computer
Science
EE
An example institutional network.
  All layer-2 broadcast traffic (ARP, unknown MAC) crosses the entire LAN
  What issues can this cause as the LAN size grows?

## Slide 5: Virtual LANs (VLANs): motivation
Computer
Science
EE
  Scalability/efficiency issues
    Non-trivial overhead from broadcast for larger LANs
  Security/privacy/admin issues
    Diverse groups of users
    It may not be okay for different groups to see each other’s traffic.
An example institutional network.

## Slide 6: Virtual LANs (VLANs): motivation
Computer
Science
EE
  Why not use routers instead?
An example institutional network.

## Slide 7: Virtual LANs (VLANs): motivation
Computer
Science
EE
  Why not use routers instead?
An example institutional network.

## Slide 8: Virtual LANs (VLANs): motivation
  Why not use routers instead?
  Makes mobility difficult.
  E.g., a CS user moves office to EE, but still belongs to the CS “group” in terms of the properties of its network connectivity.
An example institutional network.
EE
Computer
Science

## Slide 9: Virtual LAN (VLANs)
Define the set of “users” that belong in the same LAN
  i.e., users for whom it is ok for them to share a broadcast domain.
Each will become one virtual LAN (VLAN).
Configure the physical switches so that they can act as a virtual switch for each VLAN.
So, you’ll have multiple VLANs over a single physical LAN infrastructure.

## Slide 10: Port-based VLANs
1
8
2
7
9
16
10
15
a single physical switch ……
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
… operates as multiple virtual switches
1
8
2
7
EE (VLAN ports 1-8)
…
9
16
10
15
…
CS (VLAN ports 9-15)
traffic isolation:
  frames to/from ports 1-8 (EE VLAN) can only reach ports 1-8.
dynamic membership: ports can be dynamically assigned among VLANs
VLAN defined based on ports:
  The operator will specify which switch ports belong to a specific VLAN
    1-8 for EE, 9-15 for CS
  Any endpoint connected to that port will be part of that VLAN

## Slide 11: Port-based VLANs
An example institutional network.
EE
Computer
Science
All ports belong to the CS VLAN
1
2
3
4
5
Ports 1,2, 3, 5 belong to the EE VLAN
Port 4 belongs to the CS VLAN

## Slide 12: Sidenote: Other VLAN definition criteria
We can also define VLAN based on MAC addresses of endpoints, rather than switch port
  whenever a device attaches to a port, the port is connected into the appropriate VLAN based on the MAC address of the device

## Slide 13: Make sure you know
The motivation behind VLANs
What a port-based VLAN mean and how it provides traffic isolation.

## Slide 14: Port-based VLANs
An example institutional network.
EE
Computer
Science
All ports belong to the CS VLAN
1
3
5
12
2
Ports 1-8 belong to the EE VLAN
Ports 9-15 belong to the CS VLAN
B
A
How do we forward traffic between A and B?
All ports (except 1) belong to the CS VLAN
1

## Slide 15: Forwarding between VLANs
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
VLANs are separate L2 networks
So, traffic forwarding between them happens via routing
  just as with separate switches

## Slide 16: Forwarding between VLANs
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
In practice, there is not a separate physical router
The vendors sell combined switches plus routers.
So, traffic going between different VLANs will be processed by a “L3 router” within the same device.
1
8
2
7
EE (VLAN ports 1-8)
…
9
16
10
15
…
CS (VLAN ports 9-15)
+
+

## Slide 17: Port-based VLANs
EE
Computer
Science
1
3
5
12
2
Ports 1-8 belong to the EE VLAN
Ports 9-15 belong to the CS VLAN
B
A
How do we forward traffic between A and C?
  Both belong to CS VLAN, not attached to the same switch
How about between B and D?
Ports 4, 6, 7, 8 belong to CS VLAN
Ports 2, 3, 5 belong to EE VLAN
8
4
6
5
C
D
An example institutional network.
All ports belong to the CS VLAN

## Slide 18: Port-based VLANs
An example institutional network.
EE
Computer
Science
1
3
5
12
2
Ports 1-8 belong to the EE VLAN
Ports 9-15 belong to the CS VLAN
B
A
How do we forward traffic between A and C?
  Both belong to CS VLAN, not attached to the same switch
How about between B and D?
All ports belong to the CS VLAN
Ports 4, 6, 7, 8 belong to CS VLAN
Ports 2, 3, 5 belong to EE VLAN
8
4
6
5
C
D
Traffic on these ports can be from multiple VLANs

## Slide 19: VLANS spanning multiple switches
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
5
8
2
7
…
16
1
6
3
4
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
trunk port: carries frames from multiple VLANs
  So, it can help carry frames between users of a VLAN defined over multiple physical switches.
  How do we know which frame belongs to which VLAN?
    We need extra information in the link layer header.

## Slide 20: 802.1Q VLAN frame format
Original Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
2-byte Tag Protocol Identifier
(value in hex: 81-00)
Tag Control Information (2 bytes)
(12 bit VLAN ID field, 3 bit priority field like IP TOS)
Recomputed
CRC
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 21: VLANS spanning multiple switches
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
5
8
2
7
…
16
1
6
3
4
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
trunk port: carries frames from multiple VLANs
  802.1q protocol adds/removed additional header fields (i.e., the VLAN tag) for frames forwarded between trunk ports.
  The sending switch will add the tag when sending frames on the trunk port (e.g., switch on the left when sending out of port 16).
  The receiving switch will read (parse) the information and then remove it from the frame (e.g., switch on the right when receiving on port 1).

## Slide 22: Make sure you know
How traffic is forwarded between endpoints in different VLANs
How traffic is forwarded between endpoints in the same VLAN
  When they are attached to the same switch
  When they are attached to different switches

## Slide 23: VLAN Exercise
1
2
3
1
2
3
1
2
3
A
B
S1
S2
S3
C
D
E
A, C, and D are in VLAN 1, B and E are in VLAN 2.
For S1, port 1 belong to VLAN 1, port 2 belongs to VLAN 2, port 3 is a trunk port.
For S2, port 1 is a trunk port, port 2 is a trunk port, port 3 belongs to VLAN 1.
For S3, port 3 is a trunk port, port 1 belongs to VLAN 1, port 2 belongs to VLAN 2.
A sends an ARP request to find the MAC address for a certain IP address. For every switch port, find out if the ARP request will be sent out of that port or not, and if yes, does it include a VLAN tag. If yes, include which VLAN the tag represents.
Do the same exercise for the scenario in which B sends out an ARP request.

## Slide 24: Answer (for A)
A’s ARP request is a broadcast frame. It will enter S1 from port 1.
S1 will send it only out of port 3
  Port 2 belongs to a different VLAN. Broadcast frames are not sent to their incoming port.
  Port 3 is a trunk port, so there will be a VLAN tag for VLAN 1 on the frame.
S2 receives the ARP request and removes the VLAN tag.
  It will send it on port 3 as it belongs to VLAN 1. There will be no tag (it is not a trunk port).
  It will also send it on port 2, with a tag for VLAN 1.
S3 receives the ARP request and removes the VLAN tag.
  It will send it on port 1, without a tag.

## Slide 25: Answer (for B)
B’s ARP request is a broadcast frame. It will enter S1 from port 2.
S1 will send it only out of port 3
  Port 1 belongs to a different VLAN.
  Broadcast frames are not sent to their incoming port.
  Port 3 is a trunk port, so there will be a VLAN tag for VLAN 2 on the frame.
S2 receives the ARP request and removes the VLAN tag.
  It will only send it on port 2, with a tag for VLAN 2.
S3 receives the ARP request and removes the VLAN tag.
  It will send it on port 2, without a tag.

## Slide 26: EVPN: Ethernet VPNs (aka VXLANs)
In our example institutional network, a CS user could move to a different buildings inside the campus and, using VLANs, still have the “illusion” of being part of the CS L2 network.
What if the user goes home and still wants to be part of the CS L2 network?
  Why? E.g., if you want to access some server on campus, you need to be “inside” the campus network.

## Slide 27: EVPN: Ethernet VPNs (aka VXLANs)
1
8
2
7
9
16
10
15
…
…
Layer-2 Ethernet switches logically connected to each other (e.g., using IP as an underlay)
  Ethernet frames carried within IP datagrams between sites
  “tunneling scheme to overlay Layer 2 networks on top of Layer 3 networks ... runs over the existing networking infrastructure and provides a means to "stretch" a Layer 2 network.” [RFC 7348]
5
8
2
7
…
6
3
4
16
1
Sunnyvale
data center
Bangalore
data center
Ethernet
Ethernet
frame
IP
datagram

## Slide 28: What you need to know about EVPNs
Nothing for exam purposes 