## Slide 1: CS 456/656 Computer Networks
Mina Tahmasbi Arashloo and Uzma Maroof
Fall 2025
Lecture 9: Network Layer – Part 1

## Slide 2: A note on the slides
Adapted from the slides that accompany this book.
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
All material copyright 1996-2023
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 3: Network layer: roadmap
Network layer overview
Routing algorithms
Network layer in the Internet

## Slide 4: Network layer: roadmap
Network layer overview
  Network-layer service
  Addressing, routing, and forwarding
Routing algorithms
Network layer in the Internet

## Slide 5: Network-layer services
sending process
data
receiving process
data
application
transport
direct channel
network
transport
seder-side of transport protocol
receiver-side
of transport protocol
The transport layer does not concern itself with how data gets from the sending host to the receiving host.
It assumes there is a direct channel between the two.
But in reality, there is rarely a direct channel between every pair of hosts in a network…
  Q: why?
Notes: Reminding them that direct links between every pair of points does not scale

## Slide 6: Network-layer services
sending process
data
receiving process
data
application
transport
direct channel
network
transport
seder-side of transport protocol
receiver-side
of transport protocol
Notes: Reminding them that direct links between every pair of points does not scale

## Slide 7: Network-layer services
Provide the “illusion” of a direct channel between the sending and receiving host to the transport layer over a shared network.
On the end hosts:
  Sender encapsulates transport segments into datagrams and passes them to the link layer.
  Receiver extracts segments from datagrams and delivers them to the transport layer.
Through the network:
  All routers run network layer protocols and transmit datagrams from source to destination
segment
transport
direct channel
network
segment
Datagram
Datagram
Notes: Reminding them that direct links between every pair of points does not scale

## Slide 8: Network-layer channel guarantees
example for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example for a flow of datagrams:
(e.g., all datagrams belonging to the same transport-layer connection)
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing
Q: What kinds of guarantees can this “channel” provide?

## Slide 9: Example of channel guarantees
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Network-Layer Service Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
No loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
No guarantees on:
  successful datagram delivery to destination
  timing or order of delivery
  bandwidth available to end-end flow
Internet “best effort” service model
Quality of Service (QoS) Guarantees ?
Notes: Simplicity of the mechanism
Sufficient bandwidth
Bandwidth-adaptive application protocols; content distribution networks

## Slide 10: Example of channel guarantees
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Network-Layer Service Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
No loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
Quality of Service (QoS) Guarantees ?

## Slide 11: Network layer: roadmap
Network layer overview
  Network-layer service
  Addressing, routing, and forwarding
Routing algorithms
Network layer in the Internet

## Slide 12: Network-layer services
Provide the “illusion” of a direct channel between the sending and receiving host to the transport layer over a shared network.
How?
segment
transport
direct channel
network
segment
Datagram
Datagram
Notes: Reminding them that direct links between every pair of points does not scale

## Slide 13: How does the network-layer ”implement” a direct channel between a sender and receiver?
Addressing:
  Each host needs an identifier so the network can distinguish between traffic from/to different hosts.
Routing:
  Determine the “best” path from the source to the destination host
Forwarding:
  Move packet along the path, i.e., on each router, move packets from the input link to the appropriate output link
segment
transport
direct channel
network
segment
Datagram
Datagram
Notes: Reminding them that direct links between every pair of points does not scale

## Slide 14: Addressing
We will discuss addressing over the Internet in depth later.
For now, assume each host has a special identifier
  Over the Internet, these are IP addresses.
Towards host A
A
destination address included in the arriving packet.

## Slide 15: Routing
Determine the “best” path from the source to the destination host
Done by routing algorithms
E.g., router R1 should send packets going to host A on its link #2.
Towards host A
1
2
3
4
routing algorithm
Destination
output link
A
B
C
D
2
3
2
1
local forwarding table
A
destination address included in the arriving packet.
R1

## Slide 16: Routing
Towards host A
1
2
3
4
routing algorithm
Destination
output link
A
B
C
D
2
3
2
1
local forwarding table
A
destination address included in the arriving packet.
Determine the “best” path from the source to the destination host
Done by routing algorithms
E.g., router R1 should send packets going to host A on its link #2.
Routing algorithms populate forwarding tables
R1

## Slide 17: Forwarding
Moving arriving packets from router’s input link to appropriate router output link
Towards host A
1
2
3
4
A
destination address included in the arriving packet.
R1

## Slide 18: Forwarding
Moving arriving packets from router’s input link to appropriate router output link
Based on information in the forwarding table
Happens concurrently between multiple input and output links at very high speed!
  Millions of packets per second
Towards host A
1
2
3
4
A
destination address included in the arriving packet.
routing algorithm
Destination
output link
A
B
C
D
2
3
2
1
local forwarding table
R1

## Slide 19: Routing vs. Forwarding
Routing:
Determining paths to get packets to their destination
Populate forwarding tables of routers/switches
Forwarding :
Moving arriving packets from router’s input link to appropriate router output link
Towards host A
1
2
3
4
A
destination address included in the arriving packet.
Global action
Local action
R1

## Slide 20: Network layer: roadmap
Network layer overview
Routing algorithms
  Link state
  Distance vector
Network layer in the Internet

## Slide 21: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets traverse from given initial source host to final destination host
“good”: least “cost”, “fastest”, “least congested”
routing: a “top-10” networking challenge!
mobile network
enterprise
network
national or global ISP
datacenter
network
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical

## Slide 22: Graph abstraction: link costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
ci,j: cost of direct link connecting i and j
e.g., cw,z = 5, cu,z = ∞
  cost defined by network operator: could always be 1, or inversely related to bandwidth, or related to congestion
N: set of routers or “end points” connected to a router
{ u, v, w, x, y, z, a, b, c }
E: set of links =
{ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z), (u,a), (w,b), (z,c) }
a
1
1
1
c
b

## Slide 23: Routing algorithms approaches
link state: all routers have complete topology and link cost info
Distance vector:
  Routers only know about the state of their attached neighbors
  Gets updated through an iterative process of computation and exchanging info with neighbors

## Slide 24: Network layer: roadmap
Network layer overview
Routing algorithms
  Link state
  Distance vector
Network layer in the Internet

## Slide 25: Link-state routing algorithms
Two components
  Information propagation
  Path computation
Information propagation
  Each node lets the other nodes know about what it is directly connected to and at what cost
  This way, each node can build a picture of what the network graph looks like
Path computation
  Each node can use its local view of the complete network graph to compute the least-cost path to each destination

## Slide 26: Link-state routing – Information Propagation
Each router periodically generates a message including
  It’s “ID” (not the same as network-layer identifies such as IP addresses)
  All the nodes (routers and sets of end hosts) it is directly connected to
  The “cost” of the links connecting it to its direct neighbors
Information is propagated to all router
  The message is sent to the neighbors
  The neighbors will send it to their neighbors
  …
Eventually, all routers will have the same info
  Topology, link costs, which routers are connected to which end hosts

## Slide 27: Link-state routing – Information Propagation
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
a
1
1
1
c
b
y
x
w
z
1
1
2

## Slide 28: Link-state routing – Information Propagation
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
a
1
1
1
c
b
Z is connected to
{(c, 1), (w, 5), (y, 2)}
y
x
w
z
1
1
2

## Slide 29: Link-state routing – Information Propagation
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
a
1
1
1
c
b
Z is connected to
{(c, 1), (w, 5), (y, 2)}
y
x
w
z
1
1
2
5
c
1

## Slide 30: Link-state routing – Information Propagation
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
a
1
1
1
c
b
Z is connected to
{(c, 1), (w, 5), (y, 2)}
y
x
w
z
1
1
2
5
c
1

## Slide 31: Link-state routing – Information Propagation
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
a
1
1
1
c
b
Z is connected to
{(c, 1), (w, 5), (y, 2)}
y
x
w
z
1
1
2
5
c
1
This continuously happens across all nodes…
Each node generates messages
  Both periodically and when something changes
Each node forwards the updates it receives to its neighbors
So, each node finally builds an accurate picture of the network

## Slide 32: Link-state routing – Path computation
Each router computes least cost paths from itself to all other nodes
  So, it will know the least-cost path to reach each end host
  When it gets a datagram destined to a certain end host, it knows which link it should forward the datagram to.
Since every router will (eventually) have the same local version of the topology, the path they pick independently will (eventually) be consistent with each other.
How does the router compute the least-cost path?
  Well-known graph algorithms
  Classic approach, Dijkstra’s algorithm (covered in your algorithms course)

## Slide 33: Computing least-cost paths: Dijkstra’s algorithm
Runs on each router
Computes least-cost paths from that router to all other nodes
iterative: after k iterations, know least cost path to k destinations
It iterates until it knows least-cost paths to all destinations.
cx,y: direct link cost from node x to y; = ∞ if not direct neighbors
D(v): current estimate of cost of least-cost-path from source to destination v
N': set of nodes whose least-cost-path definitively known
notation

## Slide 34: Computing least-cost paths: Dijkstra’s algorithm
1 Initialization:
2 N' = {u} /* router u computes least cost path from itself to all other nodes */
3 for all nodes v
4 if v adjacent to u /* u initially knows direct-path-cost only to direct neighbors */
5 then D(v) = cu,v /* but may not be minimum cost! */
6 else D(v) = ∞
7
8 Loop
9
10
11
12
13
14
15 until all nodes in N'
find a not in N' such that D(a) is a minimum
add a to N'
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
/* least-path-cost to b either stays the same or is updated to
the known least-cost-path to a plus direct-cost from a to b */

## Slide 35: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
D(w),p(w)
5,u
4,x
3,y
3,y
v
w
x
y
z
For simplicity, we are removing the end point nodes from the graph since they are only reachable through the router they are connected to
a
1
1
b
1
c

## Slide 36: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
D(w),p(w)
5,u
4,x
3,y
3,y
5,u
∞
∞
1,u
2,u
u
v
w
x
y
z
Initialization (step 0):
For all a: if a adjacent to u then D(a) = cu,a

## Slide 37: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
D(w),p(w)
5,u
4,x
3,y
3,y
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 38: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
D(w),p(w)
5,u
4,x
3,y
3,y
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
∞
2,x
4,x
2,u
D(v) = min ( D(v), D(x) + cx,v ) = min(2, 1+2) = 2
D(w) = min ( D(w), D(x) + cx,w ) = min (5, 1+3) = 4
D(y) = min ( D(y), D(x) + cx,y ) = min(inf,1+1) = 2

## Slide 39: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
D(w),p(w)
5,u
4,x
3,y
3,y
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy

## Slide 40: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
4,y
3,y
2,u
D(w) = min ( D(w), D(y) + cy,w ) = min (4, 2+1) = 3
D(z) = min ( D(z), D(y) + cy,z ) = min(inf,2+2) = 4

## Slide 41: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv

## Slide 42: Dijkstra’s algorithm: an example
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
D(w) = min ( D(w), D(v) + cv,w ) = min (3, 2+3) = 3
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y

## Slide 43: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y
uxyvw

## Slide 44: Dijkstra’s algorithm: an example
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
D(z) = min ( D(z), D(w) + cw,z ) = min (4, 3+5) = 4
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y
uxyvw
4,y

## Slide 45: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y
uxyvw
4,y
uxyvwz

## Slide 46: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y
uxyvw
4,y
uxyvwz
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )

## Slide 47: Computing least-cost paths
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
4,x
3,y
3,y
u
y
x
w
v
z
resulting least-cost-path tree from u:
resulting forwarding table in u:
a
b
c
…
(u,a)
(u,x)
(u,x)
…
destination
outgoing link
route from u to a directly
route from u to all other destinations via x
a
1
1
b
1
c
a
1
1
b
1
c

## Slide 48: Dijkstra’s algorithm: another example
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v),
p(v)
0
1
2
3
4
5
D(w),
p(w)
D(x),
p(x)
D(y),
p(y)
D(z),
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
ties can exist (can be broken arbitrarily)
uwxvyz
v
w
x
y
z

## Slide 49: Routing based on least-cost: oscillations possible
when link costs depend on traffic volume, route oscillations possible
a
d
c
b
1
1+e
e
0
e
1
1
0
0
initially
a
d
c
b
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
a
d
c
b
given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
a
d
c
b
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
sample scenario:
  routing to destination a, traffic entering at d, c, b with rates 1, e (<1), 1
  link costs are directional, and volume-dependent
e
1
1
e
1
1
e
1
1

## Slide 50: What you need to know about Link State Routing algorithms
How they work, i.e.,
  How routers disseminate information about routes
  How each router builds a full picture of the network
  How they compute paths to destinations